Brava Theater Center

Main Stage Technical Rider

2481 24th Street 				Executive Director: Anastacia Powers-Cuellar

San Francisco, CA 94110 			Programs Director: AhSa-Ti Tyehimba-Ford

Rentals Manager: Jessica V. Cabrera

tel (415) 641-7657 				Technical Director: Cian Murty

fax (415) 641-7684						technicaldirector.brava@gmail.com

www.brava.org

Seating Capacity:

Total Seats: 360

Orchestra: 250 (includes 4 wheelchair accessible. Camera location: 3 center seats removed on Mezzanine).

Balcony: 110 (Includes light/projector/sound mix section, 4 chairs can be placed center back behind the control booth)

Stage Information:

Access to Stage:

3’-6” wide Aluminum loading ramp can be placed to get to stage level (stage right off of 24th Street) through an alley. Not accessible to vehicles (metered street parking only, free after 6pm).

Loading door size: Height: 6’10”, Width: 6’

Stage height from ground: 2’6”

Additional ground level door with step (not ADA accessible) just to the right of the loading door).

There are also double doors house right from an alleyway on York Street.

Most loading is done from the front doors and to the stage along the wings.

Proscenium Arch:

Height 22’0” – Width 30’1”

Stage Dimensions:

Width:

Proscenium arch: 30’1” wide. Front apron of stage is curved.

Wall to Wall: 44’ 8” wide.

SL Proscenium Arch to SL Wall 2’ 2”

SR Proscenium Arch to SR Wall 12’ 5”

Depth:

Center Line (from back wall to edge of center stage): 28’ deep.

Plaster Line to DS apron: 17’

Plaster Line to back wall: 11’

Height:

Stage Floor to Seating Floor level: 2’ 9”

Front of proscenium pipe grid: 22’ above stage floor.

Upstage of proscenium pipe grid: 27’ above stage floor.

Rigging

We do not have a fly system.  Riggers have put up temporary pulley systems in the past. We have a certified rigger that we can highly recommend.  People can only be hung from the C-Channel beams that run upstage-downstage.  Before any rigging for a performance, client must sign the rigging waiver form.

Dressing Rooms:

Three dressing rooms are located under the stage, can fit 5-7 people each.

There is one co-ed bathroom backstage next to the stairs to the stage on house left.

Brava is currently in the process of building a large green room/dressing room area. In the meantime our studio space can also be used as another dressing room depending on availability.

Lobby

Digital Projector: Panasonic PTL 785U, LCD Projector

Projects on to rear projection screen and faces the outer lobby for audience members entering the lobby.

LED Track Lighting, dimmable

LED Corridor Lights, always on for safety

2: Par 20 fixtures lighting historical mural

Concessions bar location is fixed

Brava Box office is located in the outer lobby

One women’s restroom located at the back of the lobby to the right, has five stalls.

Ones men’s restroom located at the back of the lobby to the left, has two stalls and three urinals

Lighting Information:

Any changes made to the house plot must be returned to the house plot set up by the conclusion of the rental or event.  If this is not completed, there may be an additional charge.

Instrument Positions:

FOH catwalk #1: 44’ 9” to plaster line, 26’ 6” above stage floor

FOH catwalk #2: 54’ 1” to plaster line, 26’ 6” above stage floor

Ante Pro Thrust Grid: 22’ 0” above stage floor

Upstage Grid: 27’ 0” above stage floor

House Lights Controls:

Breakouts: SR, last row, center house of orchestra seating, control booth (3rd floor)

Dimming and Control:

96/ 2.4k ETC Sensor Dimmers

ETC Element 2 with Monitor

Fixtures and Distribution:

All circuits are 2 P&G Stage Pin

Fixtures: Please refer to Brava house lighting plot for locations.

12: 8” Fresnels, 1K

8: PAR64, 1K, Wide Flood

16: ETC 19 deg, Source Four, 575W

27: ETC 26deg, Source Four, 575W

6: ETC 36deg, Source Four, 575W

5: Sky-Cyc, 3 Section, 1K

Digital Projector:

Available for an additional rental fee.

Comes with a Blu-ray and DVD player at no extra cost.

HDMI or VGA Connections.

We do not have a computer available for rental.

Client is responsible for bringing their own adaptor to convert to VGA or HDMI (projector connection) if they bring a computer.

Sound Information:

Any changes made to the sound system must be returned to its original set up by the conclusion of the rental or event.  If this is not completed, there may be an additional charge.

QTY Type Manufacturer Model No. description:

HOUSE SYSTEM:

1 Soundcraft Si Performer Digital Live Sound Console

1 Soundcraft Multi Digital Card (for multi-track recording)

4 Speakers Meyer Sound CQ-2 flown in pairs SL and SR

2 Speakers Meyer Sound C-50P subs in SL and SR organ loft

6 Speakers Meyer Sound fill four stage fill and two BOH fill in catwalk #2

4 Monitors Meyer Sound UM-1P powered stage monitors

1 Monitors Meyer Sound UPA-1P drum fill stage monitor

2 Monitors QSC K12

2 EQ Meyer Sound CP-10 Parametric equalizers

1 Line Driver Meyer Sound LD-1A Line Driver for speakers

1 headset station ClearCom MS-232 2 channel station

4 headset ClearCom CC95 One-eared headset

4 beltpack ClearCom RS-501 XLR wired beltpack

Add-ons available upon request only:

2 Monitors Bag End TA12-CF passive stage monitors (banana plugs)

1 Amp QSC USA 1300 amp for Bag End monitors

PROCESSORS:

1 Processor Behringer MDX 4400 audio interactive dynamics processor

1 Processor DBX 166XL compressor/limitor/gate

1 EQ Ashly MQX 2310 (main L/R inserts) stereo 31 Band Graphic Equalizer

1 EQ DBX (mon 1+2) stereo 31 Band Graphic Equalizer

1 EQ Rane ME60 (mon 3+4) stereo 31 Band Graphic Equalizer

2 Delay Lexicon MPX100 (verb 1&2) dual channel processor (Reverb)

1 Delay ADA D1280 (delay 1) digital delay for 2 rear fills

PLAYBACK:

1 DVD player Sony DVP-NS575P DVD player

1 Stanton C-502 Dual CD Player

Please note that Brava has no recorder (recording available upon request)

MICROPHONES:

8 mic Shure SM57 dynamic microphone

7 mic Shure SM58 dynamic microphone

3 mic Superlux PRA-228A dynamic (drumset - toms)

1 mic Superlux PRA-218B dynamic (bass drum)

2 mic Superlux PRA-268AH condenser (overhead mics)

1 GLS ES58

5 Countryman E6 Omnidirctional Earset Mic, Lavaiier with Shure ULX receivers. Available for an additional rental fee

DIRECT BOXES

1 DI Stewart ADB-1 active direct box

2 DI Whirlwind IMP2 direct box

3 DI DOD 265 stagehand direct box

STANDS AND ACCESSORIES

15+ Mic clips

4 short boom mic stand

14+ long boom mic stand

3+ regular mic stand

3 metal music stands

1 folding music stand

2 guitar stands

1 keyboard stand and folding seat

2 speakers stands

2 podiums, one black wooden with no mic holder, and one brown wooden with no mic holder

NOTES:

• Power - There are two quad boxes backstage right and one backstage left for power. There are also two extension cords in the front of the stage.  The control booth power is at capacity and does not support AV equipment. Additional power for the control booth is located on the mezzanine and in the wing spaces on the mezzanine.

• The backdrop of the stage is either a black traveller or our white cyc (for projecting color and video). Brava also has a 30’tall by 36’ wide black scrim available for rent.

• Parking is located at San Francisco General Hospital at San Bruno & 23rd St. (2 blocks from the theater). There are one hour meters in front of the building that run Mon-Sun until 6pm.

• Please contact the Brava Theater Technical Director, Cian Murty (techicaldirector.brava@gmail.com) prior to the show to discuss your technical questions and needs and to confirm the current inventory above.